## Slide 1: Purpose of the Call
Phase 2 – Discussion with ClearSpace
Use ClearSpace's feedback to focus Phase 2 on the most valuable direction.
We want to validate:
Which part of our concept is most relevant to ClearSpace
What assumptions we should avoid
What level of detail is realistic for Phase 2
How to shape the OSIP-style proposal around industry needs
Notes: Thank you for your time. The purpose of this call is to use your feedback to focus Phase 2 on the most valuable direction. We want to validate four things: which part of our concept is most relevant to ClearSpace, which assumptions we should avoid, what level of detail is realistic for Phase 2, and how to shape the OSIP-style proposal around industry needs.

## Slide 2: Our Phase 1 Concept
Roadmap for a serviceable satellite platform
Core idea
Not one universal interface for all satellites.
Instead: a configurable product family based on mission value and orbit.
Serviceability levels
Asset class | Serviceability provision
LEO / low-value assets | EOL capture and removal
GEO high-value assets | Docking, refuelling, health monitoring
Long-life assets | Upgrade or propulsion PODs
Future platforms | Interoperable serviceability architecture
Notes: In Phase 1 we proposed a roadmap for a serviceable satellite platform. The core idea is not one universal interface for every satellite, but a configurable product family based on mission value and orbit: EOL capture and removal for LEO and low-value assets; docking, refuelling and health monitoring for high-value GEO; upgrade or propulsion PODs for long-life assets; and an interoperable serviceability architecture for future platforms.

## Slide 3: What We Think Is the Core Problem
Current IOS is limited not only by the servicer, but by the client spacecraft.
Key issues
Legacy satellites are often non-cooperative
No standard capture / service interface
Safe-mode behaviour may conflict with servicing
Propulsion system health is uncertain
GEO architecture is changing from chemical to hybrid / electric
One solution will not fit all satellite classes
Notes: Our view of the core problem: current in-orbit servicing is limited not only by servicer capability, but by the client spacecraft. Legacy satellites are often non-cooperative, there is no standard capture or service interface, safe-mode behaviour may conflict with servicing, propulsion health is uncertain, GEO architecture is shifting from chemical to hybrid and electric, and one solution will not fit all satellite classes.

## Slide 4: Phase 2 Direction We Are Considering
Main technical focus
Degraded / cooperative serviceability
We want to study whether client-side preparation improves servicing feasibility.
Concept
Fiducials / navigation aids
IOS mode
Independent Service Beacon
Known capture geometry
Clear control handover during docking
Question for ClearSpace: Is this a meaningful operational gap from your perspective?
Notes: For Phase 2 our main technical focus is degraded and cooperative serviceability: does client-side preparation measurably improve servicing feasibility? The elements are fiducials and navigation aids, an IOS mode, an independent service beacon, known capture geometry, and clear control handover during docking. Is this a meaningful operational gap from ClearSpace's perspective?

## Slide 5: RPO Monte-Carlo Study
We are considering a simulation comparing four target cases:
Case | Target | Client-side preparation
A0 | Non-cooperative target | None
A1 | Passive prepared target | Fiducials / capture geometry
A2 | Degraded cooperative target | Service Beacon
A3 | Cooperative target | IOS mode
We would vary
Tumble rate, navigation error, communication loss, latency, initial attitude and control uncertainty.
Output
Capture success, abort probability, collision risk, ΔV and capture time — combined into a safe servicing envelope.
Question for ClearSpace: Which scenario and assumptions would be most useful for ClearSpace?
Notes: We are considering a Monte-Carlo RPO simulation comparing four targets: A0 non-cooperative, A1 passively prepared with fiducials and capture geometry, A2 degraded cooperative with a service beacon, and A3 cooperative with IOS mode. We would vary tumble rate, navigation error, communication loss, latency, initial attitude and control uncertainty, and measure capture success, abort probability, collision risk, delta-V and capture time, giving a safe servicing envelope. Which scenario and assumptions would be most useful for ClearSpace?

## Slide 6: Service Beacon + IOS Mode
Service Beacon
A low-power independent module that retains minimum servicing information if the main OBC / comms are degraded.
Possible data
Spacecraft ID
Interface location / type
Basic health flag
Angular-rate estimate
IOS status
Authentication signal
IOS mode – a defined spacecraft state for servicing
Normal
Service Standby
Approach Allowed
IOS Mode
Mated
Release / Abort
Question for ClearSpace: Would this help in real servicing operations, or should we prioritise other problems?
Notes: The service beacon is a low-power independent module that keeps minimum servicing information available if the main OBC or comms are degraded: spacecraft ID, interface location and type, a basic health flag, an angular-rate estimate, IOS status and an authentication signal. IOS mode is a defined spacecraft state for servicing: Normal, Service Standby, Approach Allowed, IOS Mode, Mated, then Release or Abort. Would this help in real operations, or should we prioritise other problems?

## Slide 7: GEO Architecture Question
Our understanding
MEV could use legacy chemical GEO geometry, especially nozzle / ring features
Future GEO platforms are moving toward hybrid / all-electric architectures
This reduces reliance on accidental legacy interfaces
Future satellites may need deliberate, propulsion-independent service interfaces
GEO platform evolution
Legacy chemical
Nozzle / ring usable as capture features (e.g. MEV)
Hybrid
Fewer legacy features to rely on
All-electric
Deliberate service interface needed
Question for ClearSpace: How does ClearSpace see this transition affecting future servicing interface strategy?
Notes: Our understanding: MEV could use legacy chemical GEO geometry, especially the nozzle and launch-adapter ring. Future GEO platforms are moving toward hybrid and all-electric architectures, which reduces reliance on these accidental legacy interfaces, so future satellites may need deliberate, propulsion-independent service interfaces. How does ClearSpace see this transition affecting future interface strategy?

## Slide 8: OSAN Concept
Orbital Service & Augmentation Node – a generic service zone for high-value future platforms
Possible functions
Capture / load transfer
Navigation references
Power / data
Optional fluid interface
POD attachment
Not planned in Phase 2
A detailed universal interface design.
Instead, we may create
Generic layout
Functional requirements
Serviceability tiers
Compatibility with future GEO platforms
Question for ClearSpace: Would ClearSpace prefer this generic service-zone approach over a detailed interface design?
Notes: OSAN, the Orbital Service and Augmentation Node, is a generic service zone for high-value future platforms, potentially combining capture and load transfer, navigation references, power and data, an optional fluid interface and POD attachment. We do not plan a detailed universal interface design in Phase 2; instead we may produce a generic layout, functional requirements, serviceability tiers and a compatibility check with future GEO platforms. Would ClearSpace prefer this generic approach over a detailed interface design?

## Slide 9: Product Family Logic
Our proposed serviceability tiers:
Tier | Level | Provisions
1 | EOL-ready | MICE-like capture + fiducials
2 | Service-ready | IOS mode + communication
3 | Life-extension-ready | Refuelling / propulsion augmentation
4 | Augmentation-ready | Power / data + upgrade POD capability
Question for ClearSpace: Which serviceability level is most relevant for ClearSpace's future market vision?
Notes: We propose four serviceability tiers: EOL-ready with MICE-like capture and fiducials; service-ready with IOS mode and communication; life-extension-ready with refuelling or propulsion augmentation; and augmentation-ready with power/data and upgrade POD capability. Which level is most relevant for ClearSpace's future market vision?

## Slide 10: What We Need From ClearSpace
We would like feedback on:
Best Phase 2 technical focus
Most realistic servicing scenario
Useful assumptions for non-cooperative / degraded targets
GEO chemical vs electric transition
Whether Service Beacon / IOS mode is valuable
How detailed OSAN should be
What ClearSpace would like to see in the OSIP proposal
Notes: Specifically, we would value feedback on: the best Phase 2 technical focus; the most realistic servicing scenario; useful assumptions for non-cooperative or degraded targets; the GEO chemical-to-electric transition; whether the service beacon and IOS mode are valuable; how detailed OSAN should be; and what ClearSpace would like to see in the OSIP proposal.

## Slide 11: Proposed Output After Feedback
Depending on ClearSpace's input, we plan to deliver:
OSIP-style proposal
RPO / serviceability simulation results
Service Beacon + IOS mode concept
OSAN generic architecture
Serviceability-tier trade study
Roadmap
Study (Phase 2)
Ground demo
IOD
Product family
Notes: Depending on your input, we plan to deliver an OSIP-style proposal, RPO and serviceability simulation results, the service beacon and IOS mode concept, a generic OSAN architecture and a serviceability-tier trade study, with a roadmap from study to ground demonstration, in-orbit demonstration and finally a product family.

## Slide 12: What would make our Phase 2 result most useful from ClearSpace's perspective?
Closing question
Should we prioritise:
RPO Monte-Carlo / non-cooperative servicing analysis
Service Beacon + IOS mode concept
OSAN / future service-zone architecture
Product-family and market roadmap
Thank you – we look forward to your feedback.
Notes: To close: what would make our Phase 2 result most useful from ClearSpace's perspective? Should we prioritise the RPO Monte-Carlo and non-cooperative servicing analysis, the service beacon and IOS mode concept, the OSAN future service-zone architecture, or the product-family and market roadmap?