## Slide 1: From Concept to OSIP-Style Proposal
PHASE 2 GOAL
Client-side serviceability features for a ClearSpace roadmap
CORE OBJECTIVE
Prove which client-side serviceability features are:
Technically useful
Economically justified
Roadmap-ready
Client
Servicer
Notes: Phase 2 moves us from a concept to an OSIP-style proposal. The core objective is evidence-based: we want to prove which client-side serviceability features are technically useful, economically justified, and suitable for a ClearSpace roadmap. Everything in this deck feeds one of those three tests.

## Slide 2: Configurable Serviceability Platform Family
WHERE WE STAND · PHASE 1
One modular client-side design, scaled to each mission's value and lifetime
ADD-ON
High-value GEO
Docking
Refuelling
Health monitoring
Maximise revenue-generating life of expensive assets
ADD-ON
Long-life assets
Upgrade PODs
Propulsion PODs
Add capability or ΔV after launch instead of replacing the satellite
ADD-ON
LEO constellations
Low-cost removal interface
Minimal per-unit cost with guaranteed, debris-free disposal
BASELINE
Every satellite
Navigation aids
Capture interface
End-of-life provision
Notes: Phase 1 proposed a Configurable Serviceability Platform Family. Every satellite carries a baseline of navigation aids, a capture interface and an end-of-life provision. On top of that, mission-specific add-ons: docking, refuelling and health monitoring for high-value GEO; upgrade and propulsion PODs for long-life assets; and a low-cost removal interface for LEO constellations, where unit cost dominates.

## Slide 3: The Main Question
PHASE 2 FOCUS
What minimum client-side features allow a satellite to remain serviceable in every state?
Design for the worst day in orbit, not the best one.
Nominal
Cooperative
Healthy, attitude-controlled and communicating — servicing through planned interfaces.
Degraded
Partially cooperative
Partial OBC, power or comms failure — key service data must still be reachable.
Non-cooperative / tumbling
Non-cooperative
No control or comms, possibly tumbling — servicer relies on passive aids and robust capture.
Notes: The central Phase 2 question: what is the minimum set of client-side features that keeps a satellite serviceable not only when it is healthy, but also when it is degraded or fully non-cooperative and tumbling? Most existing interfaces assume a cooperative client. We design for the worst case.

## Slide 4: Cooperative / Degraded Serviceability Architecture
CORE INNOVATION
IOS Mode
Defined client mode that hands control to the servicer so the two vehicles never fight.
Cooperative
Independent Service Beacon
Keeps broadcasting service data even if the main OBC or comms fail.
Degraded
Navigation aids / fiducials
Passive markers enabling relative navigation with no power needed.
Non-cooperative
MICE-like capture provision
Standardised mechanical grapple point for safe, repeatable capture.
All states
OSAN
Integrated service node for high-value platforms: power, data, fluids, PODs.
High-value
A layered architecture: each element keeps the satellite serviceable one step further as its condition degrades.
Notes: Our core innovation is the combination, not any single part. IOS Mode covers the cooperative case; the independent service beacon covers degraded states; passive fiducials and a MICE-like capture provision cover non-cooperative targets; OSAN adds a full service node for high-value platforms.

## Slide 5: Service Beacon Concept
KEY ELEMENT · SERVICE BEACON
PURPOSE
Retain minimum service information even if the main OBC or comms degrade.
Main OBC / Comms
✕ degraded / offline
Service Beacon
Own power + low-rate RF, independent of the OBC
broadcast
Servicer
Plans approach and capture from beacon data
Possible beacon data
Satellite ID
Identity, owner and mission
Interface location / type
Where and how to capture
IOS state
Standby, permitted, IOS active
Basic health flags
Power, thermal, propulsion status
Angular-rate estimate
Tumble rate for capture planning
Authentication status
Only authorised servicers proceed
Notes: The service beacon is a small, independently powered transmitter. If the main on-board computer or comms degrade, it still broadcasts the minimum a servicer needs: who the satellite is, where and what the interface is, the IOS state, basic health flags, an angular-rate estimate, and whether the servicer is authenticated.

## Slide 6: IOS Mode & Docked Control
KEY ELEMENT · IOS MODE
Problem: the client must not fight the servicer during approach and capture — uncoordinated attitude control risks collision or a failed capture.
Client state flow
Normal
Own mission, own attitude control
Service Standby
Beacon active, awaiting servicer
Approach Permitted
Authenticated go for RPO
IOS Mode
Client control passive / handed over
Mated / Servicing
Joint stack, servicer in control
Verification
Health and interface checks
Release
Separation, back to Normal
ABORT — reachable from any state once servicing starts: the client returns to a safe, predictable attitude and the servicer retreats on a passively safe trajectory.
Notes: IOS Mode solves the 'two controllers' problem. The client steps through a defined state machine: Normal, Service Standby, Approach Permitted, IOS Mode where its attitude control goes passive or is handed over, Mated/Servicing, Verification, then Release. Abort is always available and drives both vehicles to a safe configuration.

## Slide 7: RPO Monte-Carlo Simulation
SIMULATION
Four client-preparation cases
A0 Unprepared target
A1 Fiducials + capture geometry
A2 Service Beacon available
A3 Full IOS Mode
Increasing client-side preparation
What we measure
Capture success
▲ maximise
Abort rate
▼ minimise
Collision risk
▼ minimise
ΔV
▼ minimise
Capture time
▼ minimise
Robustness vs tumbling
▲ maximise
Notes: We simulate rendezvous and capture against four client cases, from an unprepared target (A0) through fiducials and capture geometry (A1), an available service beacon (A2), to full IOS Mode (A3). For each we measure capture success, abort rate, collision risk, delta-V, capture time and robustness to tumbling. The difference between cases is what quantifies the value of each client-side feature.

## Slide 8: Why MeluXina HPC Helps
COMPUTE
1
single trajectory = limited insight
1000s
of cases = a serviceability envelope
Statistics, not anecdotes: where does servicing stop being feasible?
We vary
Tumble rate
Navigation noise
Beacon packet loss
Latency
Initial attitude
Control uncertainty
Output: probability maps
Tumble rate →
Nav noise →
Feasible
Not feasible
Illustrative only — not simulation results
Notes: One trajectory tells us almost nothing about robustness. On MeluXina we can run thousands of Monte-Carlo cases, varying tumble rate, navigation noise, beacon packet loss, latency, initial attitude and control uncertainty. The output is a set of probability maps — the serviceability envelope — showing where servicing remains feasible for each client case. The map on the slide is an illustration of the format, not a result.

## Slide 9: OSAN Physical Architecture
KEY ELEMENT · OSAN
Orbital Service & Augmentation Node — an integrated service zone for high-value spacecraft
OSAN
service zone
Capture / load transfer
Power / data
Optional fluid transfer
POD attachment
GOAL
Integrate existing ideas into one scalable platform concept
MICE
MASI
ASSIST
OSAN
Why it matters
One service zone instead of scattered interfaces on the bus
Modular: fit only the interfaces each mission needs
Builds on existing work rather than a new bespoke standard
Notes: OSAN is the physical side of the architecture for high-value spacecraft: one integrated zone handling capture and load transfer, power and data, optional fluid transfer and POD attachment. The aim is not to invent a new interface but to integrate existing ideas such as MICE, MASI and ASSIST into a scalable platform concept.

## Slide 10: Team Work Split
ORGANISATION
01
Systems & OSIP proposal lead
Architecture, requirements and proposal integration
02
RPO / GNC simulation
Approach and capture models for cases A0–A3
03
HPC Monte-Carlo / data analysis
MeluXina campaigns and probability maps
04
Service Beacon & communication
Beacon data content, link and independence
05
IOS Mode / docked control / OSAN
State machine, stack control, OSAN layout
06
Business, regulatory & roadmap
Cost–benefit, regulation, path to market
Notes: Six workstreams, one owner each. The systems lead integrates everything into the OSIP proposal; simulation and HPC produce the evidence; beacon and IOS/OSAN owners define the client-side features; business and regulatory turns it into a credible roadmap.

## Slide 11: OSIP Proposal Structure
DELIVERABLE
1
Executive summary
Problem, answer and ask on one page
2
Need & state of the art
Servicing market and existing interfaces
3
Innovation vs existing work
Degraded-state serviceability, not another port
4
Objectives
Measurable goals for Phase 2 and beyond
5
Technical approach / WPs
Work packages mapped to the six workstreams
6
Expected results
Serviceability envelopes and feature trade-offs
7
Risks & mitigation
Technical, programmatic and regulatory
8
Roadmap
Ground demo → IOD → market
Notes: The proposal follows the OSIP structure: executive summary, need and state of the art, innovation versus existing work, objectives, technical approach and work packages, expected results, risks and mitigation, and a roadmap from ground demonstration through in-orbit demonstration to market.

## Slide 12: We are not proposing another docking port.
FINAL MESSAGE
We are investigating the minimum spacecraft-side preparation needed to make future satellites safely serviceable — even when degraded — and turning that into a scalable platform roadmap.
Minimum preparation
Safe when degraded
Scalable roadmap
Notes: Our message: we are not proposing yet another docking port. We are investigating the minimum spacecraft-side preparation that makes future satellites safely serviceable even when degraded, and turning that into a scalable platform roadmap for ClearSpace.